## Slide 1
CS1050 — Computer Organization and Digital Design
Nanoprocessor Design
Group 23
Name | Index No.
Jayathilake P. I. K. | 240288D
Jayawardana Y. G. L. S. | 240294R
Jayawardhana J. A. R. P. | 240297E
Kalpashaka N. G. L. G. | 240312A
Implemented in Vivado · Tested on Basys 3 FPGA · Department of Computer Science and Engineering

## Slide 2
Project Overview
Objectives
Design and develop a 4-bit nanoprocessor capable of executing arithmetic, logical, and control-flow instructions.
Implement two processor versions: Optimized (resource-efficient) and Extended (feature-rich).
Expand the instruction set from 4 instructions (12-bit, 2-bit opcode) to 11 instructions (14-bit, 4-bit opcode).
Validate all components via VHDL simulation and deploy on the Basys 3 FPGA development board.
Key Features
12-bit ISA (Optimized)
4 instructions: MOVI, ADD, NEG, JZR — 2-bit opcode
14-bit ISA (Extended)
11 instructions incl. SUB, AND, OR, XOR, NOT, CMP, CMPU, MOVI, ADD, NEG, JZR — 4-bit opcode
FPGA Deployment
Implemented and tested on Basys 3 (Artix-7 XC7A35T)
Real-time Output
4-bit result displayed via seven-segment display
Modular Architecture
ROM, PC, Decoder, Register Bank, ALU, Flags — all as separate VHDL modules

## Slide 3
Instruction Set Architecture — Optimized Version (12-bit)
Optimized Version
4 instructions · 2-bit opcode · 12-bit instruction word
Instruction | Description | Opcode | Format (12-bit)
MOVI R, d | Move immediate d → R (R ∈ [0,7], d ∈ [0,15]) | 10 | 1 0 R R R 0 0 0 d d d d
ADD Ra, Rb | Ra ← Ra + Rb | 00 | 0 0 Ra Ra Ra Rb Rb Rb 0 0 0 0
NEG R | R ← −R (2's complement) (R ∈ [0,7]) | 01 | 0 1 R R R 0 0 0 0 0 0 0
JZR R, d | If R=0 → PC←d; else PC←PC+1 (d ∈ [0,7]) | 11 | 1 1 R R R 0 0 0 0 d d d

## Slide 4
Instruction Set Architecture — Extended Version
(14-bit)
Extended Version
11 instructions · 4-bit opcode · 14-bit instruction word
Instruction | Description | Opcode (4-bit) | Format (14-bit)
MOVI R, d | Move immediate d → R | 1000 | 1 0 0 0 R R R 0 0 0 d d d d
NEG R | R ← −R (2's complement) | 1001 | 1 0 0 1 R R R 0 0 0 0 0 0 0
JZR R, d | If R=0 → PC←d; else PC←PC+1 (d ∈ [−8,7]) | 1010 | 1 0 1 0 R R R 0 0 0 d d d d
ADD Ra, Rb | Ra ← Ra + Rb | 0000 | 0 0 0 0 Ra Ra Ra Rb Rb Rb 0 0 0 0
SUB Ra, Rb | Ra ← Ra − Rb | 0001 | 0 0 0 1 Ra Ra Ra Rb Rb Rb 0 0 0 0
CMPU Ra, Rb | Unsigned comparison; updates GT/EQ/LT flags | 0010 | 0 0 1 0 Ra Ra Ra Rb Rb Rb 0 0 0 0
CMP Ra, Rb | Signed comparison; updates GT/EQ/LT flags | 0011 | 0 0 1 1 Ra Ra Ra Rb Rb Rb 0 0 0 0
OR Ra, Rb | Ra ← Ra ∨ Rb (bitwise OR) | 0100 | 0 1 0 0 Ra Ra Ra Rb Rb Rb 0 0 0 0
AND Ra, Rb | Ra ← Ra ∧ Rb (bitwise AND) | 0101 | 0 1 0 1 Ra Ra Ra Rb Rb Rb 0 0 0 0
XOR Ra, Rb | Ra ← Ra ⊕ Rb (bitwise XOR) | 0110 | 0 1 1 0 Ra Ra Ra Rb Rb Rb 0 0 0 0
NOT Ra | Ra ← ~Ra (bitwise complement) | 0111 | 0 1 1 1 Ra Ra Ra Rb Rb Rb 0 0 0 0

## Slide 5
Opcode Encoding — Original vs. Extended
Optimized Version — 2-bit Opcode
Instruction | Opcode
ADD / SUB | 00
NEG | 01
MOVI | 10
JZR | 11
Extended Version — 4-bit Opcode
Instruction | Opcode
ADD | 0000
SUB | 0001
CMPU | 0010
CMP | 0011
OR | 0100
AND | 0101
XOR | 0110
NOT | 0111
MOVI | 1000
NEG | 1001
JZR | 1010

## Slide 6
Opcode Encoding — Original vs. Extended
Key Architectural Differences
Feature | Optimized | Extended
Instruction Width | 12 bits | 14 bits
Opcode Width | 2 bits | 4 bits
No. of Instructions | 4 | 11
ALU Operations | ADD / NEG only | ADD, SUB, AND, OR, XOR, NOT, CMP, CMPU
Output Flags | Zero, Overflow | Zero, Overflow, GT, EQ, LT

## Slide 7
System Architecture Overview

## Slide 8
Top Module — Optimized Version
Optimized
entity Nanoprocessor is
Port (
Clk_100MHz : in STD_LOGIC;
reset : in std_logic;
result : out std_logic_vector(3 downto 0);
zero : out std_logic;
overflow : out std_logic
);
end Nanoprocessor;
Entity Interface
Sub-Modules Instantiated
program_rom
8×12-bit ROM; addressed by 3-bit PC
instruction_decoder
Decodes 12-bit instruction; issues control signals
ADD_SUB_4bit
4-bit ALU with ADD/NEG; produces zero & overflow flags
register_bank
Eight 4-bit registers (R0–R7) with sync write
flags
Registers zero/overflow flags on clock edge
slow_clock
Divides 100 MHz → ~0.5 Hz for visible stepping
mux2_4bit (×2)
Writeback selector (ALU vs immediate); PC mux
Signal Flow Summary
PC → ROM → 12-bit instruction word
Decoder issues reg_write_en, alu_sub, wb_sel_imm, pc_load
ALU output or immediate data written back to register bank
Zero flag → decoder for JZR conditional branch
mux8_4bit
Selects one of eight 4-bit inputs based on 3-bit select line

## Slide 9
Top Module — Extended Version
Feature | Optimized | Extended
Instruction width | 12-bit | 14-bit
Opcode | 2-bit | 4-bit
ALU top module | None | top_alu (new)
Comparator | Not present | Used inside top_alu
Logic unit (binOp) | Not present | AND/OR/XOR/NOT support
Flags out | zero, overflow | zero, overflow, GT, EQ, LT
Flag logic location | ADD_SUB_4bit | top_alu mux
Key Differences from Optimized
Extended Entity Interface
entity Nanoprocessor is
Port (
Clk_100MHz : in STD_LOGIC;
reset : in std_logic;
mode_sel : in std_logic;
sw_inst : in std_logic_vector(13 downto 0);
btn_step : in std_logic;
result : out std_logic_vector(3 downto 0);
zero : out std_logic;
overflow : out std_logic;
greater : out std_logic;
equal : out std_logic;
lower : out std_logic
);
end Nanoprocessor;

## Slide 10
Top Module — Extended Version
New Components Added in Extended Version
top_alu
Wrapper module combining ADD_SUB_4bit, Comparator, and Logic Unit. Selects output via 3-bit alu_op control signal.
Comparator
Performs signed and unsigned 4-bit comparison; generates GT, EQ, and LT flag signals.
Logic Unit (binOp)
Implements bitwise AND, OR, XOR, and NOT operations on 4-bit operands.

## Slide 11
Core Components — Overview
Program ROM
8-location ROM (12-bit optimized / 14-bit extended) driven by 3-bit PC address bus.
Program Counter
3-bit counter tracking the current instruction address; supports conditional load for JZR branches.
Slow Clock
Frequency divider reducing 100 MHz system clock to ~0.5 Hz for observable hardware stepping.
Instruction Decoder
Decodes the instruction word and asserts control signals: reg_write_en, alu_sub, wb_sel_imm, pc_load, alu_op.
Register Bank
Eight 4-bit registers (R0–R7) with synchronous write enable, 3-to-8 decoder for write selection, and two concurrent read ports.
ALU / Top ALU
Optimized: standalone ADD_SUB_4bit. Extended: top_alu integrating arithmetic, logic, and comparison sub-units.
Seven-Segment Display
Converts the 4-bit ALU result into BCD for real-time display on the Basys 3 seven-segment output.
Load Selector MUX
2-way 4-bit mux selecting between the ALU output and the immediate data field for register writeback.
Flags Unit
Clocked register capturing zero, overflow, and (in extended) GT/EQ/LT comparison flags from the ALU.

## Slide 12
Program ROM
Design Specification
Parameter | Value
Type | ROM (read-only memory)
Depth | 8 locations (8 instructions)
Width (Optimized) | 12 bits
Width (Extended) | 14 bits
Address input | 3-bit (from Program Counter)
Data output | 12 / 14-bit instruction word
Access type | Asynchronous (combinational)
VHDL Implementation Approach
entity program_rom is
Port ( addr : in STD_LOGIC_VECTOR (2 downto 0);
data : out STD_LOGIC_VECTOR (11 downto 0));
end program_rom;
architecture Behavioral of program_rom is
type rom_array is array (0 to 7) of std_logic_vector(11 downto 0);
constant ROM : rom_array := (
0 => "101110000000", -- MOVI R7, 0 (R7 = 0)
1 => "100010000001", -- MOVI R1, 1 (R1 = 1)
...
others => (others => '0’)
);
Role in Processor Datapath
Program ROM stores the hardcoded instruction sequence loaded at synthesis time.
The 3-bit PC address selects which of the 8 instruction words is presented to the instruction decoder on each clock cycle.
The Extended version widens the data bus to 14 bits to accommodate the 4-bit opcode and larger instruction fields.

## Slide 13
Program Counter & Address Control Logic
Program Counter
3-bit register tracking the current instruction address (0–7).
On each slow-clock rising edge: if pc_load='1' and zero flag set, loads jump target d; otherwise increments by 1.
Synchronous reset (btnC) returns PC to '000'.
Driven by the slow clock (~0.5 Hz) so execution is observable on hardware.
3-bit Adder (PC Increment)
Combinational 3-bit adder computes PC + 1 for the next sequential instruction.
Built from a chain of full adders, consistent with the structural VHDL approach used throughout.
Output fed to the PC register and to the MUX for jump target selection.
PC Multiplexer & Jump Logic
2-way MUX selects between PC+1 (sequential) and jump address d (branch taken).
Select signal: pc_load AND zero_flag — only JZR with R=0 triggers a branch.
Jump address d is encoded directly in the instruction word (bits [2:0] for optimized).
PC Control Signal Summary
Condition | pc_load | Zero flag | PC next
Normal execution | 0 | X | PC + 1
JZR, R ≠ 0 | 1 | 0 | PC + 1
JZR, R = 0 | 1 | 1 | d (jump target)
Reset | X | X | 000

## Slide 14
Slow Clock — Frequency Division
Purpose & Design
The Basys 3 oscillator generates a 100 MHz system clock. Direct use at this frequency would make register transitions invisible to the human eye.
The slow_clock module uses a counter-based frequency divider to reduce the processor's operating clock to approximately 0.5 Hz.
The enable input allows the top module to gate the slow clock output.
A 28-bit counter counts to 50,000,000 (half-period) and toggles the output, yielding ~1 Hz → ~0.5 Hz toggle rate.
Entity Interface
entity slow_clock is
Port (
clk_in : in STD_LOGIC;
enable : in STD_LOGIC
);
end slow_clock;
Frequency Division Parameters
Parameter | Value
Input clock | 100 MHz (Basys 3)
Counter width | 28 bits
Half-period count | 50,000,000
Output frequency | ~1 Hz
Effective processor step | ~0.5 Hz (one instruction per 2 s)
Purpose | Human-observable FPGA execution
Signal Flow
Clk_100MHz → slow_clock → divided clock signal → PC register clock input.
The divided clock governs all synchronous state transitions in the processor.

## Slide 15
Instruction Decoder — Optimized Version
Optimized
Decoder Inputs & Outputs
Port | Direction | Width | Purpose
instruction | in | 12-bit | Full instruction word from ROM
zero_flag | in | 1-bit | Zero flag from flags unit
reg_write_en | out | 1-bit | Enable write to register bank
reg_write_sel | out | 3-bit | Destination register address
read_sel_a | out | 3-bit | Source register Ra address
read_sel_b | out | 3-bit | Source register Rb address
alu_sub | out | 1-bit | ALU operation: 0=ADD, 1=NEG
wb_sel_imm | out | 1-bit | Writeback: 0=ALU result, 1=immediate d
pc_load | out | 1-bit | Enable PC jump (JZR)
Decoding Logic (2-bit Opcode)
Opcode = instruction[11:10] selects instruction type.
00 → ADD: reg_write_en=1, alu_sub=0, wb_sel_imm=0
01 → NEG: reg_write_en=1, alu_sub=1, wb_sel_imm=0
10 → MOVI: reg_write_en=1, wb_sel_imm=1 (immediate d = inst[3:0])
11 → JZR: pc_load=1 (branch if zero_flag=1), reg_write_en=0
Register fields: Ra/R = inst[9:7], Rb = inst[6:4]
Verification
Verified via Vivado simulation with all four instruction opcodes as stimuli; timing diagram confirmed correct control signal assertion on each instruction word.

## Slide 16
Instruction Decoder — Extended Version
Extended
Changes from Optimized Decoder
Feature | Optimized | Extended
Instruction width | 12-bit input bus | 14-bit input bus
Opcode field | inst[11:10] — 2 bits | inst[13:10] — 4 bits
Sub-opcode | Not applicable | inst[5:3] — 3 bits for alu_op
alu_op signal | 1-bit alu_sub | 3-bit alu_op for top_alu selection
New instructions | — | SUB, CMPU, CMP, OR, AND, XOR, NOT
Flag enable (flag_en) | Not present | Added to control flag register write
JZR range | d ∈ [0,7] | d ∈ [−8,7] (signed, 4 bits)

## Slide 17
Instruction Decoder — Extended Version
Extended
Extended Decoding Logic — alu_op Mapping
Opcode | Instruction | top_alu routing
0000 | ADD | ADD_SUB_4bit, alu_sel=0
0001 | SUB | ADD_SUB_4bit, alu_sel=1
0010 | CMPU | Comparator (unsigned)
0011 | CMP | Comparator (signed)
0100 | OR | Logic unit, binop_sel=00
0101 | AND | Logic unit, binop_sel=01
0110 | XOR | Logic unit, binop_sel=10
0111 | NOT | Logic unit, binop_sel=11

## Slide 18
Register Bank
Design Specification
Eight 4-bit general-purpose registers, R0 through R7.
R0 is hardwired to '0000' (read as zero; writes ignored).
Synchronous write: data written on rising clock edge when write_en='1'.
3-to-8 decoder selects the destination register using the 3-bit write_sel signal.
Two simultaneous read ports provide operands Ra and Rb to the ALU.
Entity Interface
entity register_bank is
Port (
clk, reset, enable : in std_logic;
write_en : in std_logic;
write_sel : in std_logic_vector(2 downto 0);
data_in : in std_logic_vector(3 downto 0);
read_sel_a: in std_logic_vector(2 downto 0);
read_sel_b: in std_logic_vector(2 downto 0);
data_a : out std_logic_vector(3 downto 0);
data_b : out std_logic_vector(3 downto 0)
);
end register_bank;
Internal Architecture
Eight instances of 4-bit D flip-flop registers, each with synchronous enable.
3-to-8 decoder converts write_sel to one-hot register enable.
Two 8-to-1 multiplexers (4-bit) select Ra and Rb read outputs.
Register Map
Register | Purpose
R0 | Hardwired zero (read-only)
R1–R6 | General-purpose arithmetic / logic
R7 | Primary result output (driven to LEDs)

## Slide 19
Register Bank
Verification
The timing diagram confirmed correct write-on-enable behavior.
Schematic
Eight 4-bit registers

## Slide 20
Arithmetic Logic Unit — Overview
ALU Comparison: Optimized vs. Extended
Aspect | Optimized Version | Extended Version
Top-level entity | ADD_SUB_4bit (direct) | top_alu (new wrapper module)
ADD / SUB | ADD_SUB_4bit | ADD_SUB_4bit (sub-module inside top_alu)
Bitwise ops | Not present | Logic Unit: AND, OR, XOR, NOT
Comparison | Not present | Comparator: signed & unsigned CMP, CMPU
Output selection | Single result | 3-bit alu_op mux selects among sub-units
Zero flag source | ADD_SUB_4bit directly | top_alu output mux
Flags produced | zero, overflow | zero, overflow, GT, EQ, LT

## Slide 21
Arithmetic Logic Unit — Overview
Sub-Unit Roles in Extended ALU
ADD_SUB_4bit
4-bit ripple carry adder/subtractor. ADD: B unchanged; SUB: B negated (2's complement). Generates carry, overflow, and zero flags.
Comparator
Performs unsigned (CMPU) and signed (CMP) 4-bit comparison. Generates one-hot GT, EQ, LT flag outputs. Used only for flag updates — does not write to registers.
Logic Unit (binOp)
Implements AND, OR, XOR, and NOT on 4-bit operands. Selected via 2-bit binop_sel from decoder. Result stored in Ra.

## Slide 22
ADD / SUB Unit — ADD_SUB_4bit
Design Overview
4-bit adder/subtractor built on a 4-bit Ripple Carry Adder (RCA_4bit).
alu_sel=0: standard addition (Y = A + B).
alu_sel=1: subtraction via 2's complement (Y = A + ~B + 1).
Overflow detected by XOR of carry-in and carry-out at MSB.
Zero flag asserted when all result bits are '0' (NOR of Y[3:0]).
Entity Interface
entity ADD_SUB_4bit is
Port (
A : in STD_LOGIC_VECTOR(3 downto 0);
B : in STD_LOGIC_VECTOR(3 downto 0);
alu_sel : in STD_LOGIC;
Y : out STD_LOGIC_VECTOR(3 downto 0);
carry : out STD_LOGIC;
overflow: out STD_LOGIC;
zero : out STD_LOGIC
);
end ADD_SUB_4bit;
Flag Generation Logic
Flag | Logic | Condition
zero | NOR(Y[3:0]) | Result = 0000
overflow | C_in XOR C_out (MSB) | Signed overflow
carry | C_out of bit 3 | Unsigned overflow
2's Complement Subtraction
When alu_sel=1, B is bitwise inverted and Cin=1 is injected at bit 0 of the RCA.
This implements A − B = A + (~B + 1) via the standard 2's complement technique.
Verification
Simulation confirmed overflow detection, zero flag, and correct subtraction across boundary cases (e.g., 0000 − 0001, signed overflow at 0111 + 0001).

## Slide 23
ADD / SUB Unit — ADD_SUB_4bit
Verification
Simulation confirmed overflow detection, zero flag, and correct subtraction across boundary cases (e.g., 0000 − 0001, signed overflow at 0111 + 0001).
Schematic
U1 -> 4-bit Ripple Carry Adder unit

## Slide 24
Comparator Unit (Extended Version)
Design Overview
The comparator supports both unsigned (CMPU) and signed (CMP) 4-bit comparison.
Generates three one-hot flags: GT (greater than), EQ (equal), LT (less than).
Comparison is flag-only — no result is written to the register bank.
Unsigned comparison: direct binary comparison of 4-bit values (range 0–15).
Signed comparison: interprets operands as 2's complement integers (range −8 to +7).
Entity Interface
entity comparator is
Port (
A, B : in STD_LOGIC_VECTOR(3 downto 0);
mode : in STD_LOGIC; -- 0=unsigned, 1=signed
GT, EQ, LT : out STD_LOGIC
);
end comparator;
Flag Truth Table
Condition | GT | EQ | LT
A > B (unsigned or signed) | 1 | 0 | 0
A = B | 0 | 1 | 0
A < B (unsigned or signed) | 0 | 0 | 1
Integration in top_alu
Comparator is a sub-module of top_alu, selected when alu_op = CMPU (0010) or CMP (0011).
GT/EQ/LT outputs are registered in the flags unit alongside zero and overflow.
Enables conditional program flow beyond the basic JZR zero-check.
Verification
Elaborated schematic and Vivado simulation confirmed correct flag assertion for boundary cases in both signed and unsigned modes.

## Slide 25
Logic Unit — Bitwise Operations (Extended Version)
Supported Operations
Instruction | Operation | Expression | alu_op
AND Ra, Rb | Bitwise AND | Ra ← Ra ∧ Rb | 0101
OR Ra, Rb | Bitwise OR | Ra ← Ra ∨ Rb | 0100
XOR Ra, Rb | Bitwise XOR | Ra ← Ra ⊕ Rb | 0110
NOT Ra | Bitwise NOT | Ra ← ~Ra | 0111
Entity Interface
entity logic_unit is
Port (
A, B : in STD_LOGIC_VECTOR(3 downto 0);
binop_sel: in STD_LOGIC_VECTOR(1 downto 0);
result : out STD_LOGIC_VECTOR(3 downto 0)
);
end logic_unit;
-- binop_sel: 00=OR, 01=AND, 10=XOR, 11=NOT
Implementation Notes
Implemented as a purely combinational circuit using concurrent signal assignments.
A 2-bit selection input (binop_sel) routes through a case statement to produce the correct output.
For NOT, operand B is ignored; Ra is complemented bit by bit.
Result is presented to the top_alu output mux, which selects it when alu_op indicates a logical operation.
Integration
Logic unit operates as a sub-module of top_alu alongside ADD_SUB_4bit and the Comparator.
The decoder asserts the appropriate alu_op (3-bit) and binop_sel (2-bit) based on the 4-bit opcode field.
Elaborated design schematic verified in Vivado; logic operations confirmed via simulation.

## Slide 26
Comparator Unit , Logic Unit

## Slide 27
Seven-Segment Display
Design Overview
Converts the 4-bit ALU result (0–15) into the appropriate seven-segment encoding for the Basys 3 display.
Implemented as a combinational lookup using a case statement (with select in VHDL).
Active-low segment outputs drive segments a–g of the display.
Extended version additionally uses flag LEDs (zero, overflow, GT, EQ, LT).
Entity Interface
entity seven_seg is
Port (
data_in : in STD_LOGIC_VECTOR(3 downto 0);
seg_out : out STD_LOGIC_VECTOR(6 downto 0)
);
end seven_seg;

## Slide 28
Seven-Segment Display
FPGA Pin Assignments (Basys 3)
Signal | Pin
seg[0] | W7
seg[1] | W6
seg[2] | U8
seg[3] | V8
seg[4] | U5
seg[5] | V5
seg[6] | U7
an[0] | U2
an[1] | U4
Segment Encoding (Hex 0–F)
Value | Decimal | Segments (a–g, active low)
0000 | 0 | 1000000
0001 | 1 | 1111001
0010 | 2 | 0100100
0011 | 3 | 0110000
0100 | 4 | 0011001
0101 | 5 | 0010010
0110 | 6 | 0000010
0111 | 7 | 1111000

## Slide 29
Fundamental Building Blocks — Half Adder & Full Adder
Half Adder
Adds two single-bit inputs A and B.
Sum S = A XOR B; Carry C = A AND B.
No carry-in input; used as the first stage in full adder construction.
entity HA is
Port ( A, B : in STD_LOGIC;
C, S : out STD_LOGIC );
end HA;
-- S <= A xor B; C <= A and B;
Half Adder Truth Table
A | B | S (Sum) | C (Carry)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Full Adder
Adds three bits: A, B, and carry-in C_in.
Built from two Half Adders: HA_0 sums A+B; HA_1 adds result to C_in.
S = A XOR B XOR C_in; C_out = (A AND B) OR (C_in AND (A XOR B)).
entity FA is
Port ( A, B, C_in : in STD_LOGIC;
S, C_out : out STD_LOGIC );
end FA;
-- Two HA instances:
-- HA_0: A+B -> HA0_S, HA0_C
-- HA_1: HA0_S + C_in -> S, HA1_C
-- C_out <= HA0_C or HA1_C;
Role in Processor
Full adders are chained to form the 4-bit Ripple Carry Adder used in ADD_SUB_4bit and the 3-bit PC incrementer.

## Slide 30
4-bit Ripple Carry Adder (RCA_4bit)
Chains four Full Adders in series to perform 4-bit addition. Carry propagates from LSB to MSB. Used inside ADD_SUB_4bit for both ADD and SUB operations.
3-bit Adder (PC Increment)
Specialized 3-bit RCA that computes PC + 1 for sequential instruction fetch. Hardwired to add binary '001' to the current PC value. Output fed to the PC multiplexer.
3-to-8 Decoder
Converts a 3-bit write_sel address into one-hot write-enable signals for the register bank. Ensures only one register is written per clock cycle. Gated with write_en to prevent accidental writes.
2-way 3-bit Multiplexer
Selects the next Program Counter value: either PC + 1 for sequential execution or jump address d when a JZR branch is taken. Select signal driven by pc_load AND zero_flag.
8-way 4-bit Multiplexer
Reads one of eight 4-bit register outputs from the register bank. Two instances provide operands Ra and Rb to the ALU simultaneously. Select driven by read_sel_a and read_sel_b from the decoder.
2-way 4-bit Multiplexer (Writeback)
Selects between ALU result and immediate data field d for register bank writeback. Controlled by wb_sel_imm from the instruction decoder; set high for MOVI, low for all ALU operations.
4-bit Register (D Flip-Flop)
4-bit D flip-flop with synchronous reset and write enable. Eight instances form the register bank; one instance serves as the PC register; another stores the slow-clock counter.
3-bit PC Register
3-bit variant of the D flip-flop register used to hold the current program counter address. D input driven by the PC MUX. Enable tied to the slow clock; reset tied to the centre button (btnC) on Basys 3.
Flags Unit
Clocked register capturing output flags from the ALU. Optimized version stores zero (Z) and overflow (V) from ADD_SUB_4bit. Extended version additionally stores GT, EQ, and LT comparison flags from the Comparator. flag_en input (extended only) prevents MOVI and JZR from inadvertently overwriting flag values between operations.
Fundamental Building Blocks — Overview

## Slide 31
4-bit Ripple Carry Adder (RCA_4bit)
The RCA_4bit is the core arithmetic unit responsible for the ADD and SUB operations. It is constructed from four 1-bit Full Adders.
entity RCA_4bit is
Port ( A : in STD_LOGIC_VECTOR (3 downto 0);
B : in STD_LOGIC_VECTOR (3 downto 0);
C_in : in STD_LOGIC;
S : out STD_LOGIC_VECTOR (3 downto 0);
C_out : out STD_LOGIC);
end RCA_4bit;
Fundamental Building Blocks — Adders
ADD (ctrl=0): S = A + B with carry-out.
SUB (ctrl=1): S = A + ~B + 1 via 2's complement; Cout used as borrow indicator.
Carry ripples bit-by-bit: simple and area-efficient at low clock speeds.
Forms the foundation of ADD_SUB_4bit and the 3-bit PC adder.
3-bit Adder (PC Increment)
A specialised version of the RCA designed to compute the next sequential instruction address (PC + 1).
entity Adder_3bit is
Port ( A : in STD_LOGIC_VECTOR (2 downto 0);
Y : out STD_LOGIC_VECTOR (2 downto 0));
end Adder_3bit;
architecture Behavioral of Adder_3bit is
begin
Y <= std_logic_vector(unsigned(A)+1);
end Behavioral;
Computes PC + 1 combinational on every clock cycle.
Output passed to the 2-way 3-bit MUX alongside the jump target address d.
MUX selects PC + 1 for normal sequential execution; selects d when JZR branch is taken (pc_load AND zero_flag = 1).
Implemented structurally using three cascaded Full Adder instances consistent with the rest of the datapath.

## Slide 32
3-to-8 Decoder (Register Select)
Maps a 3-bit register address to 8 unique 'Write Enable' signals for the register bank.
Integrated with the write_en signal to prevent accidental writes.
Ensures only one register is active at any time.
if (en = '1') then
case reg_sel is
when "000" => y <= "00000001";
when "001" => y <= "00000010";
when "010" => y <= "00000100";
when "011" => y <= "00001000";
when "100" => y <= "00010000";
when "101" => y <= "00100000";
when "110" => y <= "01000000";
when "111" => y <= "10000000";
when others => y <= "00000000";
end case;
else
y <= "00000000";
end if;
Address to Output Mapping
Address (reg_sel) | Output Bit High | Register Enabled
000 | Bit 0 | R0
001 | Bit 1 | R1
010 | Bit 2 | R2
011 | Bit 3 | R3
100 | Bit 4 | R4
101 | Bit 5 | R5
110 | Bit 6 | R6
111 | Bit 7 | R7
Fundamental Building Blocks — Decoders

## Slide 33
8-way 4-bit Multiplexer
Acts as the reading interface for the Register Bank, allowing the processor to access Ra and Rb values simultaneously.
Two independent 8-to-1 mux instances share the same register bank outputs but use different select signals (read_sel_a and read_sel_b).
Ra feeds ALU input A; Rb feeds ALU input B — both driven in the same clock cycle.
Implemented using a with-select concurrent signal assignment for purely combinational operation.
No latency: register values appear at ALU inputs within the same clock period as the decode stage.
2-way 3-bit Multiplexer (Jump Select)
Determines the next source for the Program Counter (PC).
Path A : PC + 1 (normal sequential execution).
Path B : Jump Address d extracted from instruction bits [2:0].
Control ; Driven by pc_load signal from the instruction decoder.
2-way 4-bit Multiplexer (Writeback)
Selects the source of data to be written back into the Register Bank.
Input 0 : ALU Result (for arithmetic / logic instructions).
Input 1 : Immediate Value d (for MOVI instruction).
Select : wb_sel_imm signal from the instruction decoder.
Fundamental Building Blocks — Multiplexers

## Slide 34
Fundamental Building Blocks — Registers
4-bit Register (D Flip-Flop)
4-bit D flip-flop with synchronous reset and enable.
On rising clock edge: if reset='1' → Q ← 0000; else if enable='1' → Q ← D.
Eight instances form the register bank; one instance is the PC register.
Additional instance stores the slow-clock counter for frequency division.
3-bit PC Register
Identical design to the 4-bit register but 3 bits wide to address 8 ROM locations.
D input driven by PC MUX output (either PC+1 or jump target d).
Enable tied to slow clock; reset tied to the centre button (btnC) on Basys 3.
entity pc_register is
Port ( clk : in STD_LOGIC;
enable : in STD_LOGIC;
reset : in STD_LOGIC;
D : in STD_LOGIC_VECTOR (2 downto 0);
Q : out STD_LOGIC_VECTOR (2 downto 0));
end pc_register;
entity register_4bit is
Port ( clk : in STD_LOGIC;
reset : in STD_LOGIC;
enable : in STD_LOGIC;
we : in STD_LOGIC;
D : in STD_LOGIC_VECTOR (3 downto 0);
Q : out STD_LOGIC_VECTOR (3 downto 0));
end register_4bit;
Common Register Behaviour
Condition | clk edge | Q output
reset = '1' | Rising | 0000 / 000 (cleared)
enable = '1', reset = '0' | Rising | D (data loaded)
enable = '0', reset = '0' | Rising | Q unchanged (hold)

## Slide 35
Fundamental Building Blocks — Flags
Flags Unit Optimized / Extended
Clocked register capturing output flags from the ALU.
Optimized: stores zero (Z) and overflow (V) from ADD_SUB_4bit.
Extended: additionally stores GT, EQ, LT from the Comparator.
flag_en input (extended only) controls when flags are updated — prevents MOVI/JZR from inadvertently overwriting flags.
Flags held stable between updates, available to the decoder each cycle.
Flags Entity (Optimized)
entity flags is
Port (
clk, enable, reset : in STD_LOGIC;
flag_en : in STD_LOGIC;
alu_zero : in STD_LOGIC;
alu_overflow : in STD_LOGIC;
Z : out STD_LOGIC;
V : out STD_LOGIC
);
end flags;
Flags Entity (Extended)
entity flags is
Port (
clk : in STD_LOGIC;
enable : in STD_LOGIC;
reset : in STD_LOGIC;
flag_en : in STD_LOGIC;
cmp_en : in STD_LOGIC;
alu_zero : in STD_LOGIC;
alu_overflow : in STD_LOGIC;
alu_GT : in STD_LOGIC;
alu_EQ : in STD_LOGIC;
alu_LT : in STD_LOGIC;
Z : out STD_LOGIC;
V : out STD_LOGIC;
GT : out STD_LOGIC;
EQ : out STD_LOGIC;
LT : out STD_LOGIC );
end flags;

## Slide 36
FPGA Pin Mappings — Basys 3
Optimized Version
Signal | Pin | Direction | Function
Clk_100MHz | W5 | in | 100 MHz system clock
reset (btnC) | U18 | in | Synchronous processor reset
led[0] | U16 | out | Result bit 0 (R7[0])
led[1] | E19 | out | Result bit 1 (R7[1])
led[2] | U19 | out | Result bit 2 (R7[2])
led[3] | V19 | out | Result bit 3 (R7[3])
led[4] | P1 | out | Zero flag
led[5] | L1 | out | Overflow flag
seg[0–6] | W7–U7 | out | Seven-segment a–g
an[0–3] | U2–W4 | out | Seven-segment anodes
Reset button
R7[3] R7[2] R7[1] R7[0]
overflow
zero
Seven segment display

## Slide 37
FPGA Pin Mappings — Basys 3
Extended Version — Additional Pins
Signal | Pin | Direction | Function
Clk_100MHz | W5 | in | 100 MHz system clock
reset (btnC) | U18 | in | Synchronous processor reset
btnU | T18 | in | Auxiliary button (extended)
sw[0–13] and sw[15] | V17–U1 and R2 | in | 15 input switches for extended ops
led[0–3] | U16–V19 | out | Result bits [3:0]
led[4] | P1 | out | Zero flag
led[5] | L1 | out | Overflow flag
led[6] | N3 | out | GT flag
led[7] | P3 | out | EQ flag
led[8] | U3 | out | LT flag
seg[0–6] / an[0–3] | W7–W4 | out | Seven-segment display
mode
Manual instructions
R7[3] R7[2] R7[1] R7[0]
overflow
zero
greater
equal
lower
Instruction push
reset

## Slide 38
Resource Utilization — Basys 3
Optimized Version
Extended Version
Comparison & Analysis
Metric | Optimized | Extended | Increase
LUTs | 28 | 100 | X3.57 - due to top_alu, comparator, and logic unit
Flip-Flops | 57 | 100 | X1.75 - additional flag registers (GT/EQ/LT)
I/O Buffers | 19 | 38 | x2 - switches + extra flag LEDs

## Slide 39
Conclusion
This project involved the successful design, simulation, and FPGA deployment of a 4-bit nanoprocessor in VHDL, progressing from a resource-optimized baseline to an extended feature-rich implementation.
Hardware Mastery
Gained hands-on understanding of all key processor components — ALU, instruction decoder, program counter, register bank, and flag handling — through structural VHDL implementation.
ISA Design
Designed and validated a complete instruction set architecture in both optimized (12-bit/2-bit opcode) and extended (14-bit/4-bit opcode) forms, covering arithmetic, logical, and control-flow operations.
VHDL Proficiency
Implemented and simulated all sub-modules in Vivado; timing diagrams confirmed correct functional behaviour for each component under all tested stimuli.
FPGA Deployment
All components passed physical integration testing on the Basys 3 development board, with real-time results observable via LEDs and the seven-segment display.
Design Trade-offs
Demonstrated quantified trade-offs: the Extended version approximately doubles LUT usage over the Optimized version, directly attributable to the three additional ALU sub-modules.
Collaborative Engineering
Effectively partitioned a complex multi-module system across four team members, integrating independently verified sub-modules into a fully functional processor.

## Slide 40
Team Contributions
Name | Index No. | Contributions | Hours
Jayathilake P. I. K. | 240288D | ALU, Seven-Segment Display, Top Module, Presentation, Report | 24
Jayawardana Y. G. L. S. | 240294R | Program ROM, Instruction Decoder, Presentation, Report | 22
Jayawardhana J. A. R. P. | 240297E | Program Counter, 3-bit Adder, Multiplexers, Report | 20
Kalpashaka N. G. L. G. | 240312A | Register Bank, 3-to-8 Decoder, Flags Unit, Report | 20
CS1050 · Group 23 · Department of Computer Science and Engineering · University of Moratuwa

## Slide 41
Thank You
Nanoprocessor Design · CS1050 · Group 23
Implemented in Vivado and tested on Basys 3 FPGA