## Slide 1
CS1050 — Computer Organization and Digital Design
Nanoprocessor Design
Group 23
Name | Index No.
Jayathilake P. I. K. | 240288D
Jayawardana Y. G. L. S. | 240294R
Jayawardhana J. A. R. P. | 240297E
Kalpashaka N. G. L. G. | 240312A
Implemented in Vivado · Tested on Basys 3 FPGA · Department of Computer Science and Engineering

## Slide 2
Project Overview
Objectives
Design and develop a 4-bit nanoprocessor capable of executing arithmetic, logical, and control-flow instructions.
Implement two processor versions: Optimized (resource-efficient) and Extended (feature-rich).
Expand the instruction set from 4 instructions (12-bit, 2-bit opcode) to 11 instructions (14-bit, 4-bit opcode).
Validate all components via VHDL simulation and deploy on the Basys 3 FPGA development board.
Key Features
12-bit ISA (Optimized)
4 instructions: MOVI, ADD, NEG, JZR — 2-bit opcode
14-bit ISA (Extended)
11 instructions incl. SUB, AND, OR, XOR, NOT, CMP, CMPU, MOVI, ADD, NEG, JZR — 4-bit opcode
FPGA Deployment
Implemented and tested on Basys 3 (Artix-7 XC7A35T)
Real-time Output
4-bit result displayed via seven-segment display
Modular Architecture
ROM, PC, Decoder, Register Bank, ALU, Flags — all as separate VHDL modules

## Slide 3
System Architecture Overview

## Slide 4
Opcode Encoding — Original vs. Extended
Optimized Version — 2-bit Opcode
Instruction | Opcode
ADD / SUB | 00
NEG | 01
MOVI | 10
JZR | 11
Extended Version — 4-bit Opcode
Instruction | Opcode
ADD | 0000
SUB | 0001
CMPU | 0010
CMP | 0011
OR | 0100
AND | 0101
XOR | 0110
NOT | 0111
MOVI | 1000
NEG | 1001
JZR | 1010

## Slide 5
Opcode Encoding — Original vs. Extended
Key Architectural Differences
Feature | Optimized | Extended
Instruction Width | 12 bits | 14 bits
Opcode Width | 2 bits | 4 bits
No. of Instructions | 4 | 11
ALU Operations | ADD / NEG only | ADD, SUB, AND, OR, XOR, NOT, CMP, CMPU, NEG
Output Flags | Zero, Overflow | Zero, Overflow, GT, EQ, LT

## Slide 6
Top Module — Optimized Version
Optimized
entity Nanoprocessor is
Port (
Clk_100MHz : in STD_LOGIC;
reset : in std_logic;
result : out std_logic_vector(3 downto 0);
zero : out std_logic;
overflow : out std_logic
);
end Nanoprocessor;
Entity Interface
Sub-Modules Instantiated
program_rom
8×12-bit ROM; addressed by 3-bit PC
instruction_decoder
Decodes 12-bit instruction; issues control signals
ADD_SUB_4bit
4-bit ALU with ADD/NEG; produces zero & overflow flags
register_bank
Eight 4-bit registers (R0–R7) with sync write
flags
Registers zero/overflow flags on clock edge
slow_clock
Divides 100 MHz → ~0.5 Hz for visible stepping
mux2_4bit (×2)
Writeback selector (ALU vs immediate); PC mux
Signal Flow Summary
PC → ROM → 12-bit instruction word
Decoder issues reg_write_en, alu_sub, wb_sel_imm, pc_load
ALU output or immediate data written back to register bank
Zero flag → decoder for JZR conditional branch
mux8_4bit
Selects one of eight 4-bit inputs based on 3-bit select line

## Slide 7
Top Module — Extended Version
Feature | Optimized | Extended
Instruction width | 12-bit | 14-bit
Opcode | 2-bit | 4-bit
ALU top module | None | top_alu (new)
Comparator | Not present | Used inside top_alu
Logic unit (binOp) | Not present | AND/OR/XOR/NOT support
Flags out | zero, overflow | zero, overflow, GT, EQ, LT
Flag logic location | ADD_SUB_4bit | top_alu mux
Key Differences from Optimized
Extended Entity Interface
entity Nanoprocessor is
Port (
Clk_100MHz : in STD_LOGIC;
reset : in std_logic;
mode_sel : in std_logic;
sw_inst : in std_logic_vector(13 downto 0);
btn_step : in std_logic;
result : out std_logic_vector(3 downto 0);
zero : out std_logic;
overflow : out std_logic;
greater : out std_logic;
equal : out std_logic;
lower : out std_logic
);
end Nanoprocessor;

## Slide 8
Top Module — Extended Version
New Components Added in Extended Version
top_alu
Wrapper module combining ADD_SUB_4bit, Comparator, and Logic Unit. Selects output via 3-bit alu_op control signal.
Comparator
Performs signed and unsigned 4-bit comparison; generates GT, EQ, and LT flag signals.
Logic Unit (binOp)
Implements bitwise AND, OR, XOR, and NOT operations on 4-bit operands.

## Slide 9
Program ROM
Design Specification
Parameter | Value
Type | ROM (read-only memory)
Depth | 8 locations (8 instructions)
Width (Optimized) | 12 bits
Width (Extended) | 14 bits
Address input | 3-bit (from Program Counter)
Data output | 12 / 14-bit instruction word
Access type | Asynchronous (combinational)
VHDL Implementation Approach
entity program_rom is
Port ( addr : in STD_LOGIC_VECTOR (2 downto 0);
data : out STD_LOGIC_VECTOR (11 downto 0));
end program_rom;
architecture Behavioral of program_rom is
type rom_array is array (0 to 7) of std_logic_vector(11 downto 0);
constant ROM : rom_array := (
0 => "101110000000", -- MOVI R7, 0 (R7 = 0)
1 => "100010000001", -- MOVI R1, 1 (R1 = 1)
...
others => (others => '0’)
);
Role in Processor Datapath
Program ROM stores the hardcoded instruction sequence loaded at synthesis time.
The 3-bit PC address selects which of the 8 instruction words is presented to the instruction decoder on each clock cycle.
The Extended version widens the data bus to 14 bits to accommodate the 4-bit opcode and larger instruction fields.

## Slide 10
Program Counter & Address Control Logic
Program Counter
3-bit register tracking the next instruction address (0–7).
On each slow-clock rising edge: if pc_load='1' and zero flag set, loads jump target d; otherwise increments by 1.
Synchronous reset (btnC) returns PC to '000'.
Driven by the slow clock (~0.5 Hz) so execution is observable on hardware.
3-bit Adder (PC Increment)
Combinational 3-bit adder computes PC + 1 for the next sequential instruction.
Built from a chain of full adders, consistent with the structural VHDL approach used throughout.
Output fed to the PC register and to the MUX for jump target selection.
PC Multiplexer & Jump Logic
2-way MUX selects between PC+1 (sequential) and jump address d (branch taken).
Select signal: pc_load AND zero_flag — only JZR with R=0 triggers a branch.
Jump address d is encoded directly in the instruction word (bits [2:0] for optimized).
PC Control Signal Summary
Condition | pc_load | Zero flag | PC next
Normal execution | 0 | X | PC + 1
JZR, R ≠ 0 | 1 | 0 | PC + 1
JZR, R = 0 | 1 | 1 | d (jump target)
Reset | X | X | 000

## Slide 11
Slow Clock — Frequency Division
Purpose & Design
The Basys 3 oscillator generates a 100 MHz system clock. Direct use at this frequency would make register transitions invisible to the human eye.
The slow_clock module uses a counter-based frequency divider to reduce the processor's operating clock to approximately 0.5 Hz.
The enable input allows the top module to gate the slow clock output.
A 26-bit counter counts to 50,000,000 (half-period) and toggles the output, yielding ~1 Hz → ~0.5 Hz toggle rate.
Entity Interface
entity slow_clock is
Port (
clk_in : in STD_LOGIC;
enable : in STD_LOGIC
);
end slow_clock;
Frequency Division Parameters
Parameter | Value
Input clock | 100 MHz (Basys 3)
Counter width | 26 bits
Half-period count | 50,000,000
Output frequency | ~1 Hz
Effective processor step | ~0.5 Hz (one instruction per 2 s)
Purpose | Human-observable FPGA execution
Signal Flow
Clk_100MHz → slow_clock → divided clock signal → PC register clock input.
The divided clock governs all synchronous state transitions in the processor.

## Slide 12
Instruction Decoder — Optimized Version
Optimized
Decoder Inputs & Outputs
Port | Direction | Width | Purpose
instruction | in | 12-bit | Full instruction word from ROM
zero_flag | in | 1-bit | Zero flag from flags unit
reg_write_en | out | 1-bit | Enable write to register bank
reg_write_sel | out | 3-bit | Destination register address
read_sel_a | out | 3-bit | Source register Ra address
read_sel_b | out | 3-bit | Source register Rb address
alu_sub | out | 1-bit | ALU operation: 0=ADD, 1=NEG
wb_sel_imm | out | 1-bit | Writeback: 0=ALU result, 1=immediate d
pc_load | out | 1-bit | Enable PC jump (JZR)
Decoding Logic (2-bit Opcode)
Opcode = instruction[11:10] selects instruction type.
00 → ADD: reg_write_en=1, alu_sub=0, wb_sel_imm=0
01 → NEG: reg_write_en=1, alu_sub=1, wb_sel_imm=0
10 → MOVI: reg_write_en=1, wb_sel_imm=1 (immediate d = inst[3:0])
11 → JZR: pc_load=1 (branch if zero_flag=1), reg_write_en=0
Register fields: Ra/R = inst[9:7], Rb = inst[6:4]
Verification
Verified via Vivado simulation with all four instruction opcodes as stimuli; timing diagram confirmed correct control signal assertion on each instruction word.

## Slide 13
Instruction Decoder — Extended Version
Extended
Changes from Optimized Decoder
Feature | Optimized | Extended
Instruction width | 12-bit input bus | 14-bit input bus
Opcode field | inst[11:10] — 2 bits | inst[13:10] — 4 bits
Sub-opcode | Not applicable | inst[5:3] — 3 bits for alu_op
alu_op signal | 1-bit alu_sub | 3-bit alu_op for top_alu selection
New instructions | — | SUB, CMPU, CMP, OR, AND, XOR, NOT
Flag enable (flag_en) | Not present | Added to control flag register write
JZR range | d ∈ [0,7] | d ∈ [−8,7] (signed, 4 bits)

## Slide 14
Instruction Decoder — Extended Version
Extended
Extended Decoding Logic — alu_op Mapping
Opcode | Instruction | top_alu routing
0000 | ADD | ADD_SUB_4bit, alu_sel=0
0001 | SUB | ADD_SUB_4bit, alu_sel=1
0010 | CMPU | Comparator (unsigned)
0011 | CMP | Comparator (signed)
0100 | OR | Logic unit, binop_sel=00
0101 | AND | Logic unit, binop_sel=01
0110 | XOR | Logic unit, binop_sel=10
0111 | NOT | Logic unit, binop_sel=11

## Slide 15
Register Bank
Design Specification
Eight 4-bit general-purpose registers, R0 through R7.
R0 is hardwired to '0000' (read as zero; writes ignored).
Synchronous write: data written on rising clock edge when write_en='1'.
3-to-8 decoder selects the destination register using the 3-bit write_sel signal.
Two simultaneous read ports provide operands Ra and Rb to the ALU.
Entity Interface
entity register_bank is
Port (
clk, reset, enable : in std_logic;
write_en : in std_logic;
write_sel : in std_logic_vector(2 downto 0);
data_in : in std_logic_vector(3 downto 0);
read_sel_a: in std_logic_vector(2 downto 0);
read_sel_b: in std_logic_vector(2 downto 0);
data_a : out std_logic_vector(3 downto 0);
data_b : out std_logic_vector(3 downto 0)
);
end register_bank;
Internal Architecture
Eight instances of 4-bit D flip-flop registers, each with synchronous enable.
3-to-8 decoder converts write_sel to one-hot register enable.
Two 8-to-1 multiplexers (4-bit) select Ra and Rb read outputs.
Register Map
Register | Purpose
R0 | Hardwired zero (read-only)
R1–R6 | General-purpose arithmetic / logic
R7 | Primary result output (driven to LEDs)

## Slide 16
Register Bank
Verification
The timing diagram confirmed correct write-on-enable behavior.
Schematic
Eight 4-bit registers

## Slide 17
Arithmetic Logic Unit — Overview
ALU Comparison: Optimized vs. Extended
Aspect | Optimized Version | Extended Version
Top-level entity | ADD_SUB_4bit (direct) | top_alu (new wrapper module)
ADD / SUB | ADD_SUB_4bit | ADD_SUB_4bit (sub-module inside top_alu)
Bitwise ops | Not present | Logic Unit: AND, OR, XOR, NOT
Comparison | Not present | Comparator: signed & unsigned CMP, CMPU
Output selection | Single result | 3-bit alu_op mux selects among sub-units
Zero flag source | ADD_SUB_4bit directly | top_alu output mux
Flags produced | zero, overflow | zero, overflow, GT, EQ, LT

## Slide 18
ADD / SUB Unit — ADD_SUB_4bit
Design Overview
4-bit adder/subtractor built on a 4-bit Ripple Carry Adder (RCA_4bit).
alu_sel=0: standard addition (Y = A + B).
alu_sel=1: subtraction via 2's complement (Y = A + ~B + 1).
Overflow detected by XOR of carry-in and carry-out at MSB.
Zero flag asserted when all result bits are '0' (NOR of Y[3:0]).
Entity Interface
entity ADD_SUB_4bit is
Port (
A : in STD_LOGIC_VECTOR(3 downto 0);
B : in STD_LOGIC_VECTOR(3 downto 0);
alu_sel : in STD_LOGIC;
Y : out STD_LOGIC_VECTOR(3 downto 0);
carry : out STD_LOGIC;
overflow: out STD_LOGIC;
zero : out STD_LOGIC
);
end ADD_SUB_4bit;
Flag Generation Logic
Flag | Logic | Condition
zero | NOR(Y[3:0]) | Result = 0000
overflow | C_in XOR C_out (MSB) | Signed overflow
carry | C_out of bit 3 | Unsigned overflow
2's Complement Subtraction
When alu_sel=1, B is bitwise inverted and Cin=1 is injected at bit 0 of the RCA.
This implements A − B = A + (~B + 1) via the standard 2's complement technique.
Verification
Simulation confirmed overflow detection, zero flag, and correct subtraction across boundary cases (e.g., 0000 − 0001, signed overflow at 0111 + 0001).

## Slide 19
ADD / SUB Unit — ADD_SUB_4bit
Verification
Simulation confirmed overflow detection, zero flag, and correct subtraction across boundary cases (e.g., 0000 − 0001, signed overflow at 0111 + 0001).
Schematic
U1 -> 4-bit Ripple Carry Adder unit

## Slide 20
Comparator Unit (Extended Version)
Design Overview
The comparator supports both unsigned (CMPU) and signed (CMP) 4-bit comparison.
Generates three one-hot flags: GT (greater than), EQ (equal), LT (less than).
Comparison is flag-only — no result is written to the register bank.
Unsigned comparison: direct binary comparison of 4-bit values (range 0–15).
Signed comparison: interprets operands as 2's complement integers (range −8 to +7).
Entity Interface
entity comparator is
Port (
A, B : in STD_LOGIC_VECTOR(3 downto 0);
mode : in STD_LOGIC; -- 0=unsigned, 1=signed
GT, EQ, LT : out STD_LOGIC
);
end comparator;
Flag Truth Table
Condition | GT | EQ | LT
A > B (unsigned or signed) | 1 | 0 | 0
A = B | 0 | 1 | 0
A < B (unsigned or signed) | 0 | 0 | 1
Integration in top_alu
Comparator is a sub-module of top_alu, selected when alu_op = CMPU (0010) or CMP (0011).
GT/EQ/LT outputs are registered in the flags unit alongside zero and overflow.
Enables conditional program flow beyond the basic JZR zero-check.
Verification
Elaborated schematic and Vivado simulation confirmed correct flag assertion for boundary cases in both signed and unsigned modes.

## Slide 21
Logic Unit — Bitwise Operations (Extended Version)
Supported Operations
Instruction | Operation | Expression | alu_op
AND Ra, Rb | Bitwise AND | Ra ← Ra ∧ Rb | 0101
OR Ra, Rb | Bitwise OR | Ra ← Ra ∨ Rb | 0100
XOR Ra, Rb | Bitwise XOR | Ra ← Ra ⊕ Rb | 0110
NOT Ra | Bitwise NOT | Ra ← ~Ra | 0111
Entity Interface
entity logic_unit is
Port (
A, B : in STD_LOGIC_VECTOR(3 downto 0);
binop_sel: in STD_LOGIC_VECTOR(1 downto 0);
result : out STD_LOGIC_VECTOR(3 downto 0)
);
end logic_unit;
-- binop_sel: 00=OR, 01=AND, 10=XOR, 11=NOT
Implementation Notes
Implemented as a purely combinational circuit using concurrent signal assignments.
A 2-bit selection input (binop_sel) routes through a case statement to produce the correct output.
For NOT, operand B is ignored; Ra is complemented bit by bit.
Result is presented to the top_alu output mux, which selects it when alu_op indicates a logical operation.
Integration
Logic unit operates as a sub-module of top_alu alongside ADD_SUB_4bit and the Comparator.
The decoder asserts the appropriate alu_op (3-bit) and binop_sel (2-bit) based on the 4-bit opcode field.
Elaborated design schematic verified in Vivado; logic operations confirmed via simulation.

## Slide 22
Comparator Unit , Logic Unit

## Slide 23
Seven-Segment Display
Design Overview
Converts the 4-bit ALU result (0–15) into the appropriate seven-segment encoding for the Basys 3 display.
Implemented as a combinational lookup using a case statement (with select in VHDL).
Active-low segment outputs drive segments a–g of the display.
Extended version additionally uses flag LEDs (zero, overflow, GT, EQ, LT).
Entity Interface
entity seven_seg is
Port (
data_in : in STD_LOGIC_VECTOR(3 downto 0);
seg_out : out STD_LOGIC_VECTOR(6 downto 0)
);
end seven_seg;

## Slide 24
Seven-Segment Display
FPGA Pin Assignments (Basys 3)
Signal | Pin
seg[0] | W7
seg[1] | W6
seg[2] | U8
seg[3] | V8
seg[4] | U5
seg[5] | V5
seg[6] | U7
an[0] | U2
an[1] | U4
Segment Encoding (Hex 0–F)
Value | Decimal | Segments (a–g, active low)
0000 | 0 | 1000000
0001 | 1 | 1111001
0010 | 2 | 0100100
0011 | 3 | 0110000
0100 | 4 | 0011001
0101 | 5 | 0010010
0110 | 6 | 0000010
0111 | 7 | 1111000

## Slide 25
4-bit Ripple Carry Adder (RCA_4bit)
The RCA_4bit is the core arithmetic unit responsible for the ADD and SUB operations. It is constructed from four 1-bit Full Adders.
entity RCA_4bit is
Port ( A : in STD_LOGIC_VECTOR (3 downto 0);
B : in STD_LOGIC_VECTOR (3 downto 0);
C_in : in STD_LOGIC;
S : out STD_LOGIC_VECTOR (3 downto 0);
C_out : out STD_LOGIC);
end RCA_4bit;
Fundamental Building Blocks — Adders
ADD (ctrl=0): S = A + B with carry-out.
SUB (ctrl=1): S = A + ~B + 1 via 2's complement; Cout used as borrow indicator.
Carry ripples bit-by-bit: simple and area-efficient at low clock speeds.
Forms the foundation of ADD_SUB_4bit and the 3-bit PC adder.
3-bit Adder (PC Increment)
A specialised version of the RCA designed to compute the next sequential instruction address (PC + 1).
entity Adder_3bit is
Port ( A : in STD_LOGIC_VECTOR (2 downto 0);
Y : out STD_LOGIC_VECTOR (2 downto 0));
end Adder_3bit;
architecture Behavioral of Adder_3bit is
begin
Y <= std_logic_vector(unsigned(A)+1);
end Behavioral;
Computes PC + 1 combinational on every clock cycle.
Output passed to the 2-way 3-bit MUX alongside the jump target address d.
MUX selects PC + 1 for normal sequential execution; selects d when JZR branch is taken (pc_load AND zero_flag = 1).
Implemented structurally using three cascaded Full Adder instances consistent with the rest of the datapath.

## Slide 26
3-to-8 Decoder (Register Select)
Maps a 3-bit register address to 8 unique 'Write Enable' signals for the register bank.
Integrated with the write_en signal to prevent accidental writes.
Ensures only one register is active at any time.
if (en = '1') then
case reg_sel is
when "000" => y <= "00000001";
when "001" => y <= "00000010";
when "010" => y <= "00000100";
when "011" => y <= "00001000";
when "100" => y <= "00010000";
when "101" => y <= "00100000";
when "110" => y <= "01000000";
when "111" => y <= "10000000";
when others => y <= "00000000";
end case;
else
y <= "00000000";
end if;
Address to Output Mapping
Address (reg_sel) | Output Bit High | Register Enabled
000 | Bit 0 | R0
001 | Bit 1 | R1
010 | Bit 2 | R2
011 | Bit 3 | R3
100 | Bit 4 | R4
101 | Bit 5 | R5
110 | Bit 6 | R6
111 | Bit 7 | R7
Fundamental Building Blocks — Decoders

## Slide 27
8-way 4-bit Multiplexer
Acts as the reading interface for the Register Bank, allowing the processor to access Ra and Rb values simultaneously.
Two independent 8-to-1 mux instances share the same register bank outputs but use different select signals (read_sel_a and read_sel_b).
Ra feeds ALU input A; Rb feeds ALU input B — both driven in the same clock cycle.
Implemented using a with-select concurrent signal assignment for purely combinational operation.
No latency: register values appear at ALU inputs within the same clock period as the decode stage.
2-way 3-bit Multiplexer (Jump Select)
Determines the next source for the Program Counter (PC).
Path A : PC + 1 (normal sequential execution).
Path B : Jump Address d extracted from instruction bits [2:0].
Control ; Driven by pc_load signal from the instruction decoder.
2-way 4-bit Multiplexer (Writeback)
Selects the source of data to be written back into the Register Bank.
Input 0 : ALU Result (for arithmetic / logic instructions).
Input 1 : Immediate Value d (for MOVI instruction).
Select : wb_sel_imm signal from the instruction decoder.
Fundamental Building Blocks — Multiplexers

## Slide 28
Fundamental Building Blocks — Registers
4-bit Register (D Flip-Flop)
4-bit D flip-flop with synchronous reset and enable.
On rising clock edge: if reset='1' → Q ← 0000; else if enable='1' → Q ← D.
Eight instances form the register bank; one instance is the PC register.
Additional instance stores the slow-clock counter for frequency division.
3-bit PC Register
Identical design to the 4-bit register but 3 bits wide to address 8 ROM locations.
D input driven by PC MUX output (either PC+1 or jump target d).
Enable tied to slow clock; reset tied to the centre button (btnC) on Basys 3.
entity pc_register is
Port ( clk : in STD_LOGIC;
enable : in STD_LOGIC;
reset : in STD_LOGIC;
D : in STD_LOGIC_VECTOR (2 downto 0);
Q : out STD_LOGIC_VECTOR (2 downto 0));
end pc_register;
entity register_4bit is
Port ( clk : in STD_LOGIC;
reset : in STD_LOGIC;
enable : in STD_LOGIC;
we : in STD_LOGIC;
D : in STD_LOGIC_VECTOR (3 downto 0);
Q : out STD_LOGIC_VECTOR (3 downto 0));
end register_4bit;
Common Register Behaviour
Condition | clk edge | Q output
reset = '1' | Rising | 0000 / 000 (cleared)
enable = '1', reset = '0' | Rising | D (data loaded)
enable = '0', reset = '0' | Rising | Q unchanged (hold)

## Slide 29
Fundamental Building Blocks — Flags
Flags Unit Optimized / Extended
Clocked register capturing output flags from the ALU.
Optimized: stores zero (Z) and overflow (V) from ADD_SUB_4bit.
Extended: additionally stores GT, EQ, LT from the Comparator.
flag_en input (extended only) controls when flags are updated — prevents MOVI/JZR from inadvertently overwriting flags.
Flags held stable between updates, available to the decoder each cycle.
Flags Entity (Optimized)
entity flags is
Port (
clk, enable, reset : in STD_LOGIC;
flag_en : in STD_LOGIC;
alu_zero : in STD_LOGIC;
alu_overflow : in STD_LOGIC;
Z : out STD_LOGIC;
V : out STD_LOGIC
);
end flags;
Flags Entity (Extended)
entity flags is
Port (
clk : in STD_LOGIC;
enable : in STD_LOGIC;
reset : in STD_LOGIC;
flag_en : in STD_LOGIC;
cmp_en : in STD_LOGIC;
alu_zero : in STD_LOGIC;
alu_overflow : in STD_LOGIC;
alu_GT : in STD_LOGIC;
alu_EQ : in STD_LOGIC;
alu_LT : in STD_LOGIC;
Z : out STD_LOGIC;
V : out STD_LOGIC;
GT : out STD_LOGIC;
EQ : out STD_LOGIC;
LT : out STD_LOGIC );
end flags;

## Slide 30
FPGA Pin Mappings — Basys 3
Optimized Version
Signal | Pin | Direction | Function
Clk_100MHz | W5 | in | 100 MHz system clock
reset (btnC) | U18 | in | Synchronous processor reset
led[0] | U16 | out | Result bit 0 (R7[0])
led[1] | E19 | out | Result bit 1 (R7[1])
led[2] | U19 | out | Result bit 2 (R7[2])
led[3] | V19 | out | Result bit 3 (R7[3])
led[4] | P1 | out | Zero flag
led[5] | L1 | out | Overflow flag
seg[0–6] | W7–U7 | out | Seven-segment a–g
an[0–3] | U2–W4 | out | Seven-segment anodes
Reset button
R7[3] R7[2] R7[1] R7[0]
overflow
zero
Seven segment display

## Slide 31
FPGA Pin Mappings — Basys 3
Extended Version — Additional Pins
Signal | Pin | Direction | Function
Clk_100MHz | W5 | in | 100 MHz system clock
reset (btnC) | U18 | in | Synchronous processor reset
btnU | T18 | in | Auxiliary button (extended)
sw[0–13] and sw[15] | V17–U1 and R2 | in | 15 input switches for extended ops
led[0–3] | U16–V19 | out | Result bits [3:0]
led[4] | P1 | out | Zero flag
led[5] | L1 | out | Overflow flag
led[6] | N3 | out | GT flag
led[7] | P3 | out | EQ flag
led[8] | U3 | out | LT flag
seg[0–6] / an[0–3] | W7–W4 | out | Seven-segment display
mode
Manual instructions
R7[3] R7[2] R7[1] R7[0]
overflow
zero
greater
equal
lower
Instruction push
reset

## Slide 32
Resource Utilization — Basys 3
Optimized Version
Extended Version
Comparison & Analysis
Metric | Optimized | Extended | Increase
LUTs | 28 | 100 | X3.57 - due to top_alu, comparator, and logic unit
Flip-Flops | 57 | 100 | X1.75 - additional flag registers (GT/EQ/LT)
I/O Buffers | 19 | 38 | x2 - switches + extra flag LEDs

## Slide 33
Challenges
Signed vs Unsigned Comparator
  Implementing both CMP and CMPU in one unit required separate logic paths with mode selection.
Manual Instruction Mode (Extended)
  Switching between ROM and manual instructions without glitches using mode_sel switch and Button U.
Seven-Segment with Negative Numbers
  Displaying minus sign for negative R7 required absolute value conversion before encoding.
Resource Trade-offs
  Extended version added 7 instructions → increased LUT usage while still fitting Basys 3 constraints.

## Slide 34
Team Contributions
Name | Index No. | Contributions | Hours
Jayathilake P. I. K. | 240288D | ALU, Seven-Segment Display, Top Module | 24
Jayawardana Y. G. L. S. | 240294R | Program ROM, Instruction Decoder | 22
Jayawardhana J. A. R. P. | 240297E | Program Counter, 3-bit Adder, Multiplexers | 20
Kalpashaka N. G. L. G. | 240312A | Register Bank, 3-to-8 Decoder | 20
CS1050 · Group 23 · Department of Computer Science and Engineering · University of Moratuwa

## Slide 35
Thank You
Nanoprocessor Design · CS1050 · Group 23
Implemented in Vivado and tested on Basys 3 FPGA